## Slide 1
SMART WATER
FOUNTAIN

## Slide 2
Iot devices
01
02
04
03
PH sensor
Temperature sensor
LCD
Automatic water pump

## Slide 3
01
Overview:
water pump
Here python script is used for automatic pump generation
Temperature
s
Our goal is to sense the temperature using python script
Lcd display
This 20*4 LCD display screen is going to be used to display the relevant information
A pH sensor is one of the most essential tools that's typically used for water measurements.
PH sensor

## Slide 4
PH-sensor:
PH value is a valued indicator of water quality. This PH-sensor[7] works with 5V voltage,which is also compatible with the temperature sensor. It can 6measure the PH value from 0 to 14 with an accuracy of +-0.1 at the temperature of 25 degrees.

## Slide 5
import serial
import time
port = serial.Serial("/dev/ttyAMA0", baudrate=9600, timeout=1.0)
def value():
x = 10
for i in range(x):
rcv = port.readline()
if len(rcv) > 4:
a = True
break
else:
x = x + 1
while a:
value = rcv.split(',')
# print value
ph = value[0]
Coding :

## Slide 6
w = value[1]
l = value[2]
t = value[3]
__, ph = ph.split(':')
__, w = w.split(':')
__, l = l.split(':')
__, t = t.split(':')
ph = float(ph)
w = float(w)
l = float(l)
t = float(t)
a = False
return ph, w, l, t
while True:
print(value())
time.sleep(2)

## Slide 7
Temperature sensor :
A water-proof temperature sensor is going to be used. Part number from spark fun is DS18B20 [6]. This temperature sensor is compatible with a relatively wide range of power supply from 3.0V to 5.5V. The measured temperature ranges from -55 to +125 celsius degrees. Between -10 to + 85 degrees, the accuracy is up to +-0.5 degrees. This sensor can fulfill all requirements needed for this project.

## Slide 8
import time
from w1thermsensor import W1ThermSensor
sensor = W1ThermSensor()
while True:
temperature= sensor.get_temperature.()
print("The temperature is %s celsius" % temperature)
time.sleep(1)
Coding:

## Slide 9
The design of the circuit for Interfacing 16×2 LCD with Raspberry Pi is very simple. First, connect pins 1 and 16 of the LCD to GND and pins 2 and 15 to 5V supply. Then connect a 10KΩ Potentiometer to pin 3 of the LCD, which is the contrast adjust pin. The three control pins of the LCD i.e. RS (Pin 4), RW (Pin 5) and E (Pin 6) are connected to GPIO Pin 7 (Physical Pin 26), GND and GPIO Pin 8 (Physical Pin 24).
LCD:

## Slide 10
#!/usr/bin/env python
import RPi.GPIO as GPIO
from time import sleep
# Define GPIO to LCD mapping
LCD_RS = 7
LCD_E = 8
LCD_D4 = 25
LCD_D5 = 24
LCD_D6 = 23
LCD_D7 = 18
# Define some device constants
LCD_WIDTH = 16 # Maximum characters per line
LCD_CHR = True
LCD_CMD = False
LCD_LINE_1 = 0x80 # LCD RAM address for the 1st line
LCD_LINE_2 = 0xC0 # LCD RAM address for the 2nd line
# Timing constants
E_PULSE = 0.0005
E_DELAY = 0.0005
Coding :

## Slide 11
def main():
# Main program block
GPIO.setwarnings(False)
GPIO.setmode(GPIO.BCM) # Use BCM GPIO numbers
GPIO.setup(LCD_E, GPIO.OUT) # E
GPIO.setup(LCD_RS, GPIO.OUT) # RS
GPIO.setup(LCD_D4, GPIO.OUT) # DB4
GPIO.setup(LCD_D5, GPIO.OUT) # DB5
GPIO.setup(LCD_D6, GPIO.OUT) # DB6
GPIO.setup(LCD_D7, GPIO.OUT) # DB7
# Initialise display
lcd_init()
while True:
# Send some test
lcd_string("Electronics Hub ",LCD_LINE_1)
lcd_string(" Presents ",LCD_LINE_2)
sleep(3) # 3 second delay
# Send some text
lcd_string("Rasbperry Pi",LCD_LINE_1)
lcd_string("16x2 LCD Test",LCD_LINE_2)
sleep(3) # 3 second delay

## Slide 12
# Send some text
lcd_string("1234567890*@$#%&",LCD_LINE_1)
lcd_string("abcdefghijklmnop",LCD_LINE_2)
sleep(3)
def lcd_init():
lcd_display(0x28,LCD_CMD) # Selecting 4 - bit mode with two rows
lcd_display(0x0C,LCD_CMD) # Display On,Cursor Off, Blink Off
lcd_display(0x01,LCD_CMD) # Clear display
sleep(E_DELAY)
def lcd_display(bits, mode):
# Send byte to data pins
# bits = data
# mode = True for character
# False for command
GPIO.output(LCD_RS, mode) # RS
# High bits
GPIO.output(LCD_D4, False)

## Slide 13
GPIO.output(LCD_D5, False)
GPIO.output(LCD_D6, False)
GPIO.output(LCD_D7, False)
if bits&0x10==0x10:
GPIO.output(LCD_D4, True)
if bits&0x20==0x20:
GPIO.output(LCD_D5, True)
if bits&0x40==0x40:
GPIO.output(LCD_D6, True)
if bits&0x80==0x80:
GPIO.output(LCD_D7, True)
# Toggle 'Enable' pin
lcd_toggle_enable()
# Low bits
GPIO.output(LCD_D4, False)
GPIO.output(LCD_D5, False)
GPIO.output(LCD_D6, False)
GPIO.output(LCD_D7, False)
if bits&0x01==0x01:
GPIO.output(LCD_D4, True)
if bits&0x02==0x02:
GPIO.output(LCD_D5, True)
if bits&0x04==0x04:
GPIO.output(LCD_D6, True)
if bits&0x08==0x08:
GPIO.output(LCD_D7, True)
# Toggle 'Enable' pin
lcd_toggle_enable()
def lcd_toggle_enable():
# Toggle enable
time.sleep(E_DELAY)

## Slide 14
GPIO.output(LCD_E, True)
time.sleep(E_PULSE)
GPIO.output(LCD_E, False)
time.sleep(E_DELAY)
def lcd_string(message,line):
# Send string to display
message = message.ljust(LCD_WIDTH," ")
lcd_display(line, LCD_CMD)
for i in range(LCD_WIDTH):
lcd_display(ord(message[i]),LCD_CHR)
if __name__ == '__main__':
try:
main()
except KeyboardInterrupt:
pass
finally:
lcd_display(0x01, LCD_CMD)
GPIO.cleanup()

## Slide 15
The motor gets automatically switched on when water in the overhead tank (OHT) falls below the lower limit. Similarly, it gets switched off when the tank is filled up.
Water pump:

## Slide 16
from classes import Hardware
from classes import TimeKeeper as TK
import schedule
import smtplib
import time
import ssl
# WATERING_TIME must be in "00:00:00 PM" format
WATERING_TIME = '11:59:50 AM'
SECONDS_TO_WATER = 10
RELAY = Hardware.Relay(12, False)
EMAIL_MESSAGES = {
'last_watered': {
'subject': 'Raspberry Pi: Plant Watering Time',
'message': 'Your plant was last watered at'
},
'check_water_level': {
'subject': 'Raspberry Pi: Check Water Level',
'message': 'Check your water level!',
}
}
def send_email(time_last_watered, subject, message):
port = 465
smtp_server = "smtp.gmail.com"
FROM = TO = "YOUR_EMAIL@gmail.com"
password = "YOUR_PASSWORD"
Coding:

## Slide 17
complete_message = ''
if time_last_watered == False:
complete_message = "Subject: {}\n\n{}".format(subject, message)
else:
complete_message = "Subject: {}\n\n{} {}".format(subject, message, time_last_watered)
context = ssl.create_default_context()
with smtplib.SMTP_SSL(smtp_server, port, context=context) as server:
server.login(FROM, password)
server.sendmail(FROM, TO, complete_message)
def send_last_watered_email(time_last_watered):
message = EMAIL_MESSAGES['last_watered']['message']
subject = EMAIL_MESSAGES['last_watered']['subject']
send_email(time_last_watered, subject, message)
def send_check_water_level_email():
message = EMAIL_MESSAGES['check_water_level']['message']
subject = EMAIL_MESSAGES['check_water_level']['subject']
send_email(False, subject, message)

## Slide 18
def water_plant(relay, seconds):
relay.on(
time.sleep(seconds)
print("Watering is finished!")
relay.off()
def main():
time_. = TK.TimeKeeper(TK.TimeKeeper.get_current_time())
if(time_keeper.current_time == WATERING_TIME):
water_plant(RELAY, SECONDS_TO_WATER)
time_keeper.set_time_last_watered(TK.TimeKeeper.get_current_time())
print("\nPlant was last watered at {}".format(time_keeper.time_last_watered))
# send_last_watered_email(time_keeper.time_last_watered)
# schedule.every().friday.at("12:00").do(send_check_water_level_email)
while True:
# schedule.run_pending()
time.sleep(1)
main()

## Slide 19
THANK YOU